Lab Re-Entry Checklist

Remove any posted hibernation notifications Flush your eyewash for 10 minutes to ensure that the lines are clear Clean and disinfect lab benches. Be sure to make fresh disinfection solutions. Is the room free of odors? Flush cup sinks to reduce odors from dry traps. Check for signs of utility failure (e.g. power outage, etc.). Check refrigerators and freezers to see if they are working properly. Caution, odors may build up during an extended hibernation. Check room and local ventilation. You can perform a qualitative check by using a tissue/kimwipe to see if your fume hood or local exhaust are working. Check any running equipment for damage or power failure (e.g. pumps, glove boxes, anaerobic chambers, etc.). Check that all systems left under an atmosphere of inert gas are still inert. Inspect the integrity of gas/water tubing to make sure they are free from cracks and leaks Check the integrity of all chemical containers. Clean any residue seen on the outside of the bottle and check the quality of chemicals if the container integrity has been compromised. Dispose of any chemicals that are expired or where the quality is suspect. Test peroxide-forming chemicals that are open prior to re-use. If working with radioactive materials, complete a post-hibernation radiation survey. Then notify Radiation Safety, who will help reconcile your reports. If you work with controlled substances, check for expired drugs and label the appropriately. Contact cshelp@umn.edu with any questions Make sure BSC certification is up-to-date. BSC annual re-certification may be delayed due to lab hibernation. Please contact Biosafety for lab inspection which is required for PI's new IBC application or amendment.

Contact Facilities Management, 612-624-2900, with any facility concerns

Contact University Health and Safety, 612-626-6002, with any laboratory safety concerns